## Slide 1
DIGITAL
DESIGN &
CIRCUIT
ANALYSIS
ONE-ZONE RULE-BASED
SECURITY CLASSIFICATION
Design and Simulation of a Smart Home Security System
A digital-logic-based approach to combining security sensor conditions and classifying situations as Safe, Warning, Intrusion, or Emergency.
Logisim Simulation
AND / OR / NOT Logic
Single Security Zone
Student Names & Roll Numbers: [Name 1 – Roll No.] | [Name 2 – Roll No.]
Guide: [Guide Name]
Department: [Department Name] | [College Name]
Academic Year: 2026–27

## Slide 2
2. Introduction
Background, domain overview, and why the problem matters
CONTEXT
The real-world setting
A home security zone contains several signals that describe what is happening: door status, motion, forced entry, heat, and whether the system is armed.
The design challenge
A sensor signal is often ambiguous by itself. The useful question is not just “did a sensor trigger?” but “what situation do these signals describe together?”
Our project focus
We implement a small, rule-based decision system in digital logic that turns a combination of binary inputs into a security classification and final alarm condition.
Think of the circuit as a tiny security decision-maker:
Sensors
System state
Conditions
Situation
Alarm
The “smart” part is the rule-based interpretation — not AI or machine learning.

## Slide 3
3. Problem Statement
Why a simple sensor-to-alarm rule is not enough
PROBLEM
Basic idea
Sensor triggered
→ immediate alarm
Why this can be limiting
• A door opening can be normal activity, not necessarily an intrusion.
• Motion alone does not always explain why the motion occurred.
• Forced entry and dangerous heat represent different kinds of threats.
• Treating every event identically loses useful context.
What the project asks instead:
What happened?
Door / Motion / Forced Entry / Heat
What is the system state?
Armed or Disarmed
How serious is it?
Safe / Warning / Intrusion / Emergency

## Slide 4
4. Objectives
Specific goals of the project
OBJECTIVES
01
Model one security zone
Represent the armed state and four sensor inputs as binary signals.
02
Classify situations
Distinguish Safe, Warning, Intrusion, and Emergency conditions.
03
Use multi-condition logic
Combine sensor states instead of treating every trigger identically.
04
Implement digitally
Translate the rules into Boolean logic and gates in Logisim.
05
Validate behavior
Test representative combinations and verify the resulting outputs.
06
Keep the design extensible
Show how the same zone logic could later be replicated for multiple zones.

## Slide 5
5. Literature Survey / Existing System
Common approaches and the gap addressed by our design
EXISTING
Approach
Basic idea
Limitation / observation
Conventional trigger-based alarm
Individual sensor activation can directly trigger an alarm.
Simple and easy to implement, but context is limited.
Zoned security systems
Sensors are grouped by protected areas and monitored by a control panel.
Better organization, but the decision rules may still be relatively simple.
Multi-sensor / sensor-fusion approaches
Several measurements are combined to improve situation awareness.
More informative, but often much more complex than a first-year logic circuit.
Position of our project
We are not claiming a new commercial security technology; we demonstrate a small, rule-based multi-condition classifier using digital logic.

## Slide 6
6. Proposed System
From raw binary inputs to a meaningful security state
PROPOSED
Inputs
A
Armed / Disarmed
D
Door Open
M
Motion
F
Forced Entry
H
Heat
RULE-BASED
SECURITY LOGIC
Combines armed state + sensor conditions
to classify the current situation.
AND / OR / NOT
SAFE
Routine / no active threat
WARNING
Relevant event, not yet intrusion
INTRUSION
Strong evidence of unauthorized entry
EMERGENCY
Heat-related emergency condition
Final alarm condition is derived from the applicable higher-severity security state.

## Slide 7
7. System Architecture / Block Diagram
Signal flow for one security zone
ARCHITECTURE
Zone Inputs
ARMED
System state
DOOR
Door sensor
MOTION
Motion sensor
FORCED ENTRY
Intrusion sensor
HEAT
Heat sensor
Condition & State Logic
Warning path
Armed + Door Open
Intrusion path
Armed + Door + Motion
Intrusion path
Forced Entry
Emergency path
Heat condition
Boolean gates implement the conditions above; the classification logic then feeds the alarm output.
SAFE
State output
WARNING
State output
INTRUSION
State output
EMERGENCY
State output
FINAL ALARM

## Slide 8
8. Methodology / Implementation
How the real-world requirement becomes a digital circuit
METHOD
1
Define inputs
Armed, Door, Motion, Forced Entry, Heat
2
Define states
Safe, Warning, Intrusion, Emergency
3
Write rules
Describe which input combinations correspond to each state
4
Translate to Boolean logic
Use AND, OR, and NOT to implement the rules
5
Build in Logisim
Connect gates and outputs for one security zone
6
Test combinations
Verify representative scenarios and edge cases
Key principle
The circuit is deterministic: the same input combination always produces the same classification.

## Slide 9
9. Results and Discussion
Representative test cases and expected circuit behavior
RESULTS
Case
A
D
M
F
H
Situation
Expected state
Comment
Normal
0
0
0
0
0
No active security event
SAFE
Disarmed / idle
Door while armed
1
1
0
0
0
Open door
WARNING
Suspicious but not yet intrusion
Door + motion
1
1
1
0
0
Open door + movement
INTRUSION
Stronger combined evidence
Forced entry
1
0
0
1
0
Direct intrusion signal
INTRUSION
High-confidence trigger
Heat
1
0
0
0
1
Dangerous heat
EMERGENCY
Different threat category
Disarmed activity
0
1
1
0
0
Normal activity
SAFE*
Security response disabled
* Exact disarmed behavior follows the final truth table / logic implemented in the submitted circuit.
Evidence to insert
Replace / supplement this slide with your actual Logisim screenshot and final truth table before submission.
Discussion: the key result is not merely “alarm ON”; it is the distinction between different conditions using combined inputs.

## Slide 10
10. Conclusion
What the project achieves
CONCLUSION
We converted a real-world security problem into a deterministic digital decision system.
Problem addressed
A simple “any sensor → alarm” approach does not distinguish ordinary activity from stronger evidence of intrusion or a different emergency.
What we changed
We introduced rule-based multi-condition classification using the armed state and several sensor signals.
What we demonstrated
The rules can be represented with Boolean logic and implemented as a one-zone circuit in Logisim.
What it is not
It is not AI, machine learning, IoT, phone-connected automation, or a physical sensor system.
How it scales
The same zone-level logic can be replicated and combined to form a larger multi-zone system.
Core takeaway
Inputs → conditions → situation → alarm

## Slide 11
References & Submission Notes
Use these as background references; add course-specific sources used by your team
REFERENCES
Digital logic foundations
1. M. Morris Mano & Michael D. Ciletti, Digital Design: With an Introduction to the Verilog HDL.
2. Thomas L. Floyd, Digital Fundamentals.
Use your prescribed textbook / lecture notes as the primary academic source for Boolean logic, combinational circuits, and truth tables.
Security / sensor-combination background
Use introductory references on intrusion detection, alarm systems, and sensor fusion to motivate the design. Keep the literature discussion proportional to a first-year project; the main contribution is the circuit implementation.
Before final submission
Replace the name/roll-number placeholders. Insert your actual Logisim circuit screenshot. Replace the representative result table with the final verified test cases / truth table from your circuit. Ensure terminology exactly matches your implemented logic, especially the behavior when the system is disarmed.
Thank you